## Slide 1: Dynamic Partial Reconfiguration for Fault-Tolerance in automotive ECUs
Andreas Hirtenlehner, Rupert Schorn, Peter Schober, Constantin Schieber

## Slide 2: Introduction
Electronic Control Units (ECU) in automotive
Control tasks like
  Ignition
  ESP
  ABS
Often, redundancy is required

## Slide 3: Introduction (optional)
https://financialcounselor24.com/2018/08/automotive-electronic-control-unit-ecu-market-2018-mro-490353/

## Slide 4: Purpose and Goal of our System
Hardware redundancy is expensive
Provide redundancy with FPGA
In case of malfunction: Instantiate ECU in FPGA
  Same code
  Same communication channel
  No one should notice malfunction

## Slide 5: Designed Architecture

## Slide 6: Designed Architecture (malfunction)

## Slide 7: Progress
Instantiated a Cortex M1 Core on FPGA and toggle LEDs
Same with Microblaze Core as backup
Obtained Cortex M0 and M3 boards, CAN Transceivers and I2C ADC
Defined custom Bus-Protocol
Wrote MCU Application Code

## Slide 8: Zedboard Quick Demo (optional)
Time
Reset PL with Button
Cortex A9
Programmable Logic
Cortex M1
AXI
GPIO LED
Drive 1 LED
Cortex A9
Programmable Logic
Cortex M1
AXI
GPIO LED
Drive 1 LED
1 LED
active
3 LEDs
active
FSBL
PL Bitstream
BOOT.bin
SD CARD

## Slide 9: Faced Problems and their Solutions (1/2)
ARM Designstart
Modify Blockdiagram
BSP
Modify Software
Generate next Bitstream
Time
Vivado
Xilinx SDK
Arm Keil
Vivado
Reprogramming of instantiated Softcore implies re-synthesis
    Inconvenience due to free licence
  Possible Solution: Replace Keil with SDK
    Problem: Correctly configure SDK. E.g. Toolchain

## Slide 10: Faced Problems and their Solutions (2/2)
Application
ARM Mbed OS
Xilinx FPGA Core
STM32 MCU
Find common Codebase for MCU and Xilinx Core
    Problem: ARM Mbed OS does not support Xilinx Cores
    Possible Solutions:
Application
Custom HAL
Xilinx FPGA Core
STM32 MCU
Xilinx BSP
STM32 HAL
Port Mbed to Xilinx Core
Design custom HAL

## Slide 11: Future Plan
FPGA Cortex M1/3
  Systic Timer
  I2C-IP
  CAN-IP
FPGA Health Monitor
Design Middleware
  port Mbed or design custom HAL
Realize Hardware Setup

## Slide 12: Potential for Collaboration
Partial Dynamic Reconfiguration
  With other PDR group
  Will also use static and dynamic partitions
  Exchange experience on PDR

## Slide 13: Thank you for your attention!

## Slide 14: Backup Slides
Einstellungen in der Keil Software
Tool Versions:
Toolchain: MDK-Lite Version: 5.26.2.0
Toolchain Path: C:\Keil_v5\ARM\ARMCC\Bin
C Compiler: Armcc.exe V5.06 update 6 (build 750)
Assembler: Armasm.exe V5.06 update 6 (build 750)
Linker/Locator: ArmLink.exe V5.06 update 6 (build 750
Library Manager: ArmAr.exe V5.06 update 6 (build 750)
Hex Converter: FromElf.exe V5.06 update 6 (build 750)
CPU DLL: SARMCM3.DLL V5.26.2.0
Dialog DLL: DARMCM1.DLL V1.19.1.0
Target DLL: UL2CM3.DLL V1.161.6.0
Dialog DLL: TARMCM1.DLL V1.14.0.0